## Slide 1: ELEC S212 (Sept. 2018) Network Programming and Design
Surgery 2
(Network Infrastructure)
Course Coordinator : Dr. Steven Choy
Tutor : Mr. Lee, Bo-sing (Joe)
URL of my teaching website : http://learn.ouhk.edu.hk/~t441051/s212

## Slide 2: Agenda for Surgery 2
What is network Infrastructure
Transmission basic
Transmission medium
Physical and logical topology
Network access method (or technology)
Network equipment (or components)
2 types of network backbone
Collision problem
Broadcast problem

## Slide 3: Objective of Unit 2
Describes the core elements of a network infrastructure;
Explains basic network signal transmission concepts;
Discusses the most appropriate transmission media in respect to different circumstances;
Describes different network topologies;
Describes different types of access networks, and identifies their differences;
Explains the functionality of networking equipment including hubs, switches and routers;
Outlines basic network design principles and tools.

## Slide 4: What is Network Infrastructure (1)
Network infrastructure is composed of
  Transmission medium
    Wired or wireless
  Physical and logical topology
    Bus, ring, star, hybrid
  Network access method (or technology)
    Etherenet (CSMA/CD), wireless (CSMA/CA), Token ring (obsolete), FDDI, ATM, etc.
  Network equipment
    Hub (obsolete), repeater, LAN switch, bridge and router
  Servers
    WWW, email, DNS, etc
  Protocol suit (TCP/IP) and NOS

## Slide 5: What is Network Infrastructure (2)
  Design of network infrastructure:
    How to connect network equipment and servers
    Where should be placed for those network equipment and servers
    Configuration of those network equipment and servers
    Configuration of NOS

## Slide 6: Types of transmission signal
Transmission is the processing required to pass signal (i.e. data) from one end to the other via transmission medium
2 types of signal
  Analog
    Signal value is continuous
    With amplitude, frequency, wavelength and phase
    Signal strength decrease with transmission length => loss of signal content
    Eg. Dialup networking or multiplexing
  Digital
    A series of pulses, with value of “0” and “1” only
    Encoding series of “0” and “1” to represent signal content

## Slide 7: transmission direction
Simplex
  Signal can travel in one direction only
Half-duplex
    Signal can travel in both direction over medium but in only one direction at a time
Full-duplex
      Signal can travel in both direction over medium but in both directions at the same time
Multiplex
  Multiple signal are allowed to travel at the same time over medium, with each signal assigned to a sub-channel.

## Slide 8: Transmission media (1)
Wired
  Coaxial cable
    BNC connector
    Used in obsolete Thinnet (10base2) & thicknet (10base5)
    HK cable TV still use RG-6 coaxial cable
  Twisted pair cable (most-commonly used)
    Relatively inexpensive, easy to install, flexible
    2 types:
      STP - With a shielding to prevent electro-magnetic interference
      UTP - cat. 1 to 7, RJ-45 connector,
    Fiber optic (growing but expensive)
    Resistant to electro-magnetic interference
    Longer transmission distance (2 to 5km), larger bandwidth (100baseFX, 1G, 10G or above)
    Better security

## Slide 9: Transmission media (2)
Cat 6/6a

## Slide 10: Transmission media (3)

## Slide 11: Transmission media (4)
Wireless
  Radio Frequency (802.11b, a, g, n)
    802.11b – up to 11 Mbps, RF is 2.4 GHz
    802.11a – up to 54 Mbps, RF is 4.8 GHz
    802.11g – up to 54 Mbps, RF is 2.4 GHz
    802.11n – up to 500 Mbps or more.
    Longer distance (100 to 150m) & better data rate
    Usually requires access point (AP)
  Blue tooth
    Version 1.x, 2.x, 3.x, 4.x, 5.x
    Exchange data over short distance with less data rate
    Lower power consumption & simpler configuration

## Slide 12: Transmission media (5)
5 factors in choosing media
  Cost
    Setup cost (Installation) + continuous cost (maintenance & support)
    reusing existing infrastructure,
  Size & Scalability
    Max. node per segment, segment length, max. network length
  Throughput and bandwidth (Speed)
    Speed of vertical (backbone) cable must be greater than that of horizontal (LAN) cable
  Ease of installation, maintenance & support
  Noise immunity
    Environmental Electro-Magnetic Interference (EMI)

## Slide 13: Physical Topology (1)
Physical topology :
  Physical view of devices (host & cable concentrating device) and cable
  The choice of the physical topology should be in alignment to the transmission media, cabling design and network type.
  Different physical topologies vary in their scalability and reliability.
  3 types:
    Bus (coaxial cable, thinnet, thicknet)
      Bad scalability
      Single point of failure
    Ring (FDDI)
      Bad scalability
      Single point of failure
    Star (UTP with hub, switch or router)
      Better scalability
      Failure of one node/link has no effect on other nodes

## Slide 14: Physical Topology (2)

## Slide 15: Logical Topology
Logical topology :
  refers to how data is transmitted back and forth among the nodes within a network.
  It is concerned with layout view in terms of signal flow
  It is related to the network access technology.
  2 types:
    Bus (eg. in Ethernet)
    Ring (eg. in Token ring)
Physical and logical topology of a network can be different.
  Eg. Token ring : Physically star, logically ring
  Eg. Ethernet : physically star, logically bus

## Slide 16: Network access technology
Many technologies are available for network access layer:
  Ethernet
    Concurrent market dominant for LAN
  Wireless
    Emerging for LAN
  Token ring
    Obsolete
  FDDI
    Obsolete network backbone
  ATM
    For WAN
  Frame Relay
    For WAN
  …..

## Slide 17: Ethernet
2 types of Ethernet
  Shared Ethernet
    Older generation
    use hub, half duplex
    cannot overcome collision => bad performance especially for large network
  Switched Ethernet
    Concurrent generation
    Use LAN switch, full duplex
    overcome collision => Better performance
Ethernet uses CSMA/CD (Carrier Sense Multi-Access/Collision Detect) for accessing media.

## Slide 18: CSMA/CD
Detail of CSMA/CD
  Each station always listens on its segment for any signal transmission or collision
  Send preamble (a sequence of 1010…bits) before actual data bits
  If 2 or more stations transmit at the same time, collision occurs and is detected. All transmitting stations stop sending immediately.
  After random of time, re-transmit
So, if any 2 stations transmit data at the same time, the transmitted data will collide and corrupted => collision.
Both stations need to re-transmit data after random of delay => bandwidth is wasted => network performance is degraded.

## Slide 19: IEEE standards for Ethernet

## Slide 20: Wireless
Use CSMA/CA, which is similar to CSMA/CD except that receiver sends explicit acknowledge to sender => more overhead but with better reliability
Each wireless network is named with a SSID (Service Set IDentifier).
Computer associates to the wireless network by this SSID

## Slide 21: Token ring (Obsolete)
Token ring media access mechanism
  When no host is sending data, a free token is traveling along the ring.
  Host must capture a free token before sending data
  After capturing a free token, host starts transmitting data
  Downstream host repeats signal from upstream host
  Transmitting host generate free token after data is received by receiver.

## Slide 22: Network equipment (1)
Computers are not connected directly. They are connected to networking devices. Devices include:
  Repeater & hub
    Operates at OSI layer 1 or TCP/IP layer 1
    What is hub (movie). Repeater regenerates electrical signal. Hub is just a multi-port repeater.
    Hub cannot overcome collision (movie) and broadcast problem.
  Transparent bridge
    Operates at OSI layer 2 or TCP/IP layer 1
    Forward frame based on destination MAC address.
    Bridge operation (movie).

## Slide 23: Network equipment (2)
  switch
    Operates at OSI layer 2 or TCP/IP layer 1
    What is switch (movie). Switch is just a multi-port bridge
    Switch/bridge can overcome collision problem (movie) but cannot overcome broadcast problem.
    Compare hub, switch in terms of collision control (movie)

## Slide 24: Network equipment (3)
  Router
    Operates at OSI layer 3 or TCP/IP layer 2
    Forward IP packet based on destination IP address
    What is router (movie)
    Router can overcome broadcast (movie) & collision problem
  Gateway – can work on all layers.

## Slide 25: Network backbone
Classification in terms of location of backbone router:
  distributed backbone -
    Backbone routers are distributed over wide area
    Higher cost to connect backbone routers using WAN
    Hard to manage
  Collapsed backbone -
    Backbone components are centralized in a single location
    Lower cost,
    easy management
    Higher adaptability
    Higher scalability

## Slide 26: LAN - Collision problem (1)
Segmentation by hub/repeater.
All computers in same collision domain => collision problem

## Slide 27: LAN - Collision problem (2)
Segmentation by switch/bridge (overcome collision problem).
Each port of switch corresponds to one segment
=> multiple small collision domains => better performance

## Slide 28: LAN - Broadcast problem (1)
All hosts are connected by hub/repeater/bridge/switch & belongs to same subnet.
Broadcast sent by any host can reach all other hosts => broadcast problem

## Slide 29: LAN - Broadcast problem (2)
router is used to connect 4 subnets.
Broadcast is limited to each subnet => broadcast domain is much less.

## Slide 30: VLAN
VLAN definition:
  A logical grouping of network nodes
Nodes can locate at different locations by connecting to different LAN devices.
All nodes of same VLAN forms a broadcast domain and belongs to same subnet
Currently, only switch supports VLAN.
Benefits of VLAN:
  Network management: easy to migrate host to another VLAN without physical relocation
  Security : communication between VLANs can be controlled.
  Limit collision & broadcast traffic within one VLAN

## Slide 31: Factors that Impact Network Performance
Size of collision domain
  Larger collision domain => lower performance
Size of broadcast domain
  Networking protocols are broadcast based
  Larger broadcast domain => lower performance
Bandwidth of your network
  Lower bandwidth => lower performance
Number of PCs of your network.
  More PC => performance may downgrade if not properly designed
Application are data-intensive or not.

## Slide 32
Open
Discussions