## Slide 1: ELEC S212 (AY_2018) Network Programming and Design
Surgery 1
(Introduction to computer networking & the Internet)
Course Coordinator : Dr. Steven Choy
Tutor : Mr. Lee, Bo-sing (Joe)
URL of my teaching website : http://learn.ouhk.edu.hk/~t441051/s212

## Slide 2: Agenda
Objective of Tutorial 1
Tutorial 1
  What is computer network
  Why computer network
  Basic computer networking concepts/terms
  Layering network model – OSI & TCP/IP
  Protocols and standards
  Internet & Internet services

## Slide 3: Objectives of surgery 1
Explain what a computer network is, and why computer networks are used.
Describe the general services that computer networks provide or facilitate.
Describe, compare and contrast the characteristics of client/server architecture and peer-to-peer architecture.
Categorize networks according to scale, and explain their differences.
Describe the basic network topologies, and explain the benefits and uses of different topologies.
Describe, compare and contrast the characteristics of circuit-switched networking and packet-switched networking.

## Slide 4: Objectives of surgery 1
Describe, compare and contrast the characteristics of connection-oriented and connectionless services.
Identify and describe the more important LAN technologies.
Describe what a network operating system is, and identify its important features.
Outline, compare, and contrast the OSI model and the Internet reference model.
Explain what the Internet is, and describe its infrastructure.
Identify and describe some of the most important services that are available on the Internet.
Define the prevalent networking protocols and standards, and identify some of the more important standards organizations and Internet standards.

## Slide 5: What is computer network?
Definition of computer network
  a group of computers & networking devices (eg. Printer, fax, etc.) that are connected by some type of transmission media. The computers can communicate, provide or access shared resources, with the help of some networking S/W.
There are different resources that can be shared
  Equipment such as printer, fax, scanner
  Information such as data file, multimedia file, database, application program
  Storage
  Computational resource
  …..

## Slide 6: Why computer network?
Computer network provides many advantages:
  Share resources sharing
    Refer to previous slide
  Enhancing communication and collaboration between people
    Email, WWW, video conference
    Entertainment (network games)
    E-commerce
    Online discussion forum
  Remote management of network resources
    Network administrator at Hong Kong can remotely configure/monitor/reboot network equipments at U.S., Europe, etc.

## Slide 7: Features of a good computer network?
A good computer network should be featured with:
  Meet end user’s requirements
  Performance is accepted by end uesrs.
  Good Reliability or High availability
  Scalability
  Security
  Easy to manage
  Within budget

## Slide 8: Basic computer networking concepts
Introduction of some basic computer networking concepts/terms:
  Network classification
  Network topology
  3 types of switching methods
  Connection-oriented Vs connectionless
  Network transport system
  Network OS
  Network security

## Slide 9: Network classification
Computer network can be classified from different points of view.
Usually, we classify networks from 3 perspectives
  based on size of network:
    PAN, LAN, MAN, CAN & WAN
  based on role of network computers:
    Client/server Vs Peer-to-peer networks
  Based on transmission media:
    Wired network Vs wireless network

## Slide 10: Network classification
Classification of networks by size of network
  PAN (Personal Area Network). Eg. your home network.
  LAN (Local Area Network)
    Within an office or building
    High transmission speed.
  MAN (Metropolitan Area Network)
    Larger than LAN. Multiple LANs that extend across multiple buildings.
  CAN (Campus Area Network)
    Larger than MAN. Multiple LANs that extend across Campus.
  WAN (Wide Area Network)
    Across city, country or even international
    Connected through public data network provided by carrier
    Transmission speed of WAN link is lower than that of LAN

## Slide 11: LAN

## Slide 12: MAN/CAN

## Slide 13: WAN

## Slide 14: Network classification
Classification of networks by role of computers:
  client/server network
    Server
      is the computer that has better processing (CPU) power and more memory.
      provides services or shares its resources to clients.
    Client
      is the computer that has less processing (CPU) power and less memory.
      requests services or uses shared resources from server.
    more complex, centralized management,
    Suitable for larger company
    Eg. Active directory or domain
    (cont’d)

## Slide 15: Network classification
Classification of networks by role of computers:
  peer-to-peer network
    All computers has similar processing power and size of memory.
    Each computer can share its file storage/printer to other computer.
    Simple, decentralized management
    Suitable for small company
    eg. workgroup

## Slide 16: Network classification
Classification of networks by transmission media:
  Wired network
    Transmission media is cable
    Eg. Cat5/6 UTP, optic fiber, etc
  Wireless network
    Transmission media is through air
    Eg. RF or Infrared

## Slide 17: Network topology
Physical topology
  The physical layout of network’s nodes.
  3 basic physical topologies:
    Bus, star, ring
Logical topology
  The way in which a network access media and transmit signal across it.
  2 basic logical topologies:
    Bus, ring
A network may have different physical and logical topology.
  Eg. An Ethernet network connected with a LAN switch
    Physical topology is star
    Logical topology is bus

## Slide 18: Physical topologies (1)
Bus
Star
Ring

## Slide 19: Physical topologies (2)
 | Star | Bus | Ring
Advantage | Less costly than mesh, easier fault identification and isolation | Ease of installation, cost-effective for long line of devices | Better reliability than bus
Disadvantage | Hub failure causing total network breakdown | Difficult fault isolation, path break causing isolation into two groups of devices | Path break can disable the whole network unless if it is a dual ring
No. of links | n | 1+n | n
Application examples | Local area network in offices | Coaxial cable TV in households or buildings | Obsolete Token ring

## Slide 20: 3 types of switching methods
Switching method determines how connections are created between nodes
There are 3 types:
  Circuit switching
  Packet switching (TCP/IP)
  Message switching

## Slide 21
Circuit switching service is a telecommunication technology
  by which two network nodes establish a dedicated (i.e. non-shared) communications channel (or circuit) connecting them for the duration of the communication session before the nodes may communicate.
  This is done by the telephone system, using the dialed number with ordinary voice-grade lines and ISDN digital lines.
WAN technologies uses circuit switching service:
  ISDN
Circuit-switching

## Slide 22
Packet/cell switching is a digital networking communications method that groups all transmitted data – regardless of content, type, or structure – into suitably-sized blocks, called packets/cells.
  Packets/cells are then transferred in variable-bit-rate data streams (sequences of packets) over a shared WAN cloud.
  When traversing network adapters, switches, routers and other network nodes, packets are buffered and queued, resulting in variable delay and throughput depending on the traffic load in the network.
  The path is determined by the addressing field in each packet/cell and the routers/switches along the path => addressing overhead in frame encapsulation.
WAN technologies that uses packet/cell-switched service
  Frame relay, X.25, ATM & SMDS
Packet-switching

## Slide 23
Message switching is precursor of packet switching.
Message is stored and routed entirely in each hop, without partitioning into packets.
First introduced in 1961.
Message-switching

## Slide 24
Circuit-switching vs packet-switching
 | Circuit-switching | Packet-switching
cost | higher | lower
Effective usage of link bandwidth | Waste bandwidth | better
Transmission delay | Predictable & constant | un-predictable and variable
Addressing overhead in each unit of data | no | yes
Dedicate/share link | Dedicate link | Share link

## Slide 25: Connection-oriented Vs Connectionless
Connection-oriented
  A connection must be established between 2 communicating nodes before actual data transfer between these 2 nodes.
  Often provide reliable transfer of data, in proper sequence
  More transmission overhead
  statful
Connectionless (datagram communication)
  Transfer data to communicating party without establishing any connection.
  No guarantee on the data will be received by the communicating party.
  Less transmission overhead
  stateless
More will be discussed in Tutorial 3.

## Slide 26: Network Transport system
Network Transport system describes the logical interconnection, rather than physical interaction, between nodes.
It depends on the electrical pulses carried by physical layer of OSI model.
Currently, Ethernet and Wi-Fi are the 2 most common transport systems.
Legacy transport systems include ARCNET and Token ring.

## Slide 27: Layered network model (1)
In order to allow 2 computers to communicate, exchange data, share/access resource via a network, these 2 computers must follow a number of rules. The rules are so many and complicated. These rules are called networking protocols.
We need a method/mechanism to develop & handle these rules.
So, a layered network model is required for computer networking.
There are 2 networking models – OSI & TCP/IP

## Slide 28: Layered network model (2)
Logical view of a layered network model
  Network is divided into a number of layers
  Lowest layer is numbered as 1, higher layer is numbered with larger number
  Layer N (Boss) request service, layer N-1 (employee) provide service
  Each layer is ignorant about implementation of other layers
  Each layer only knows the interface (SAP) to directly lower or upper layer

## Slide 29: Layered network model (3)
Advantages
  Simplify complexity of network design & implementation
  Easy for human to discuss & analyze
  Allow interoperability between products from different vendors
  Change of any layer is transparent to other layers
  Implementation of any layer is independent of other layers

## Slide 30: OSI model

## Slide 31: OSI model

## Slide 32: TCP/IP model

## Slide 33: OSI Vs TCP/IP
Layer mapping between OSI and TCP/IP model
OSI model | Internet (TCP/IP) model
Application | application
Presentation | 
Session | 
Transport | Transport
Network | Internet
Data link | Network access
Physical | 

## Slide 34: OSI Vs TCP/IP
OSI model
  7 layers – application, presentation, session, transport, network, data link, physical layer
  Well-defined
  More restrictive in layering structure
  Transport layer can use different protocols eg. SPX for Netware
  Usually as a reference point for discussion use or academic research. Seldom implemented

## Slide 35: OSI Vs TCP/IP
Internet (TCP/IP) model
  4 layers,
    Layer 4 (Application) – dns, ftp, smtp, http, snmp, …..
    Layer 3 (Transport) – tcp, udp
    Layer 2 (Internet) – ip, icmp
    Layer 1 (Network access) – ethernet, token, FDDI , ATM
  De-facto and only standard for INTERNET
  Transport layer is dominated by TCP and UDP
  Development based on experiment & practice
  Less restrictive in layering structure

## Slide 36: More on protocol
What is protocol
  Protocol is a standard method or format for communication between network devices.
  Protocols ensure that data are
    transferred whole, in sequence, and
    without error from one node on the network to another.
Key elements of protocol
  Syntax — the structure or format of the data.
  Semantics — the meaning of each section of the data.
  Synchronization — when data should be sent and how fast they can be sent.

## Slide 37: What is Standard
Standard
  is well-documented agreements
  Contains technical specifications or other precise criteria that stipulate how a product should be designed or performed
  Different industrial vendors produce their products based standards so that networking products from different vendors can be compatible (i.e. work together).
Major standard organizations
  IEEE committee of ISO - for LAN and MAN standards (eg. Ethernet, FDDI, Wi-Fi, etc.)
  IETF – for INTERNET standards (RFC).
  ANSI – for telecommunication standards.

## Slide 38: Some RFCs

## Slide 39
Open
Discussions